## Slide 1: Basic components and Electric Circuits (chapter 2)

## Slide 3
Power is considered positive if current flow is from + sign to – sign
Power is considered negative if current flow is from – sign to + sign
For any circuit the summation of powers for all elements are equal to zero

## Slide 4
Short circuit : S.C
if a wire is connected from one terminal of an electrical element to another terminal then
We can say that there is a short circuit on that element .
Short circuit on resistor will cause current and voltage to be zero according to ohms law
Open circuit : O.C
Any cut in the wire connecting electrical elements is called open circuit this will cause current to be zero
Note : voltage may exist between the two open terminals

## Slide 5
Short Circuit as Zero Resistance
An element (or wire) with R=0 is called a short circuit
Short Circuit as Voltage Source (0V)
An ideal voltage source Vs= o v is also equivalent to a short circuit
Since v=i.R and R=0, V=0 regardless to I
Could draw a source with vs=0 volt but not in practice =smoke

## Slide 6: Open Circuit
An element with R=∞ is called an open circuit
Just omitted
Open Circuit as Current Source (0 A)
An ideal current source I=0A is also equivalent to an open circuit
Could draw a source with I=0A , but is not done in practice
Cannot connect a current source to an open circuit (smoke )