## Slide 1
Chapter 1
Information Sources & Sources Coding
(part 3)

## Slide 2
Chapter 1 (part 3)
Information Rate
Extension of a discrete memoryless source

## Slide 3
Information Rate
If a message source generates messages (symbols) at the rate of r messages per second, the rate of information R is defined as the average number of bits of information per second or merely information rate.
H is the average number of bits of information per message. Hence,
R = (messages per second) x (average number of bits per messages)
R = rH bits/s

## Slide 4
Let us consider two sources of equal entropy H, generating and r1 and r2 messages per second, respectively.
The first source will transmit the information at a rate R1 = r1H and the second will transmit the information at a rate R2 = r2H.
Now if r1> r2, then R1> R2. Thus in a given period, more information is transmitted from the first source than the second source, placing greater demands on the communication channel.
Hence, the source is not described by its entropy alone but also by its rate of information.
Information Rate
R = rH bits/s

## Slide 5
Extension of a discrete memoryless source
In discussing information theoretic concepts, we often find useful to consider blocks rather than individual symbols, with each block consisting of n successive source symbols.
We may view each block as being produced by an extended source alphabet.
In the case of discrete memoryless source, the source symbols are statistically independent.
  Hence, the probability of a source symbol in Sn is equal to the product of the probabilities of the n source symbols in S constituting the particular source symbol in Sn.
We may thus intuitively expect that H(Sn), the entropy of the extended source, is equal to n times H(S), the entropy of the original source.
Each block is produced by an extended source with a source alphabet Sn that has Kn distinct blocks
H(Sn) = n H(S)

## Slide 6
Example 1.3
Consider the Example 1.2 of a discrete memoryless source with source alphabet
S = {s0, s1, s2} with p0 = 1/4 , p1=1/4 and p2=1/2 .
Prove that H(S2) = 2 H(S).
Solution
We had already calculated that H(S)=3/2 bits. Now, consider the second-order extension of the source. With the source alphabet S consisting of K=3 symbols, it follows that the source alphabet S2 of the extended source has K2 = 32 = nine symbols:
    s0s0, s0s1, s0s2, s1s0, s1s1, s1s2, s2s0, s2s1, s2s2.
We may denote these symbols by 0, 1,…, 8 respectively.
H(S2) = p(0) log2[1/p(0)] + p(1) log2[1/(p(1)] + … + p(8) log2[1/p(8)]
= (1/16) log2[16] + (1/16) log2[16] + (1/8) log2[8] + (1/16) log2[16]
+ (1/16) log2[16] + (1/8) log2[8] + (1/8) log2[8] +(1/8) log2[8] +(1/4) log2[4]
= 3 bits= 2 H(S)
H(S2) = 2 H(S)
The probability of these nine source symbols are 1/16, 1/16, 1/8, 1/16, 1/16, 1/8, 1/8, 1/8, and 1/4 respectively.